## Slide 1: Multiply and Divide
Integers in 2’s compliment
Floating point

## Slide 2: Multiplying in Decimal
214  2.14 x
x 21  2.1 x
------- multiply mantissa
214 add exponents
+ 4280
-------- -----------------
4494  4.494 x

## Slide 3: Multiplying in binary
1011 11
x 1110 x 14
------- -------
0000 44
1011 11
1011
1011
----------- ------------
10011010 154

## Slide 4: History of binary multiplication
Until late 1970’s most processors did not have a multiply instruction. Programs that repeated shifted and added were used instead.
When much more transistors per chip became available, enough adders could be put on a single chip to um all the partial products at once. Rather than reuse a single adder repeatedly.

## Slide 5: 2 by 2 multiplication chip

## Slide 6: 4 by 4 multiplication chip

## Slide 7: Multiplying floating point numbers
  sign exp fraction
  0 1001 010  1.01 x
  0 0111 110  1.11 x
  ------------
  10.0011 x
  Convert from 2’s compliment to scientific notation
    - create mantissa by putting a 1 to the left of fraction
    - subtract bias (7) from the exponents
  Multiple mantissas
  Add exponents
  Adjust exponent so mantissa starts 1.xxxx
  Add bias to exponent
  Fraction is the significant bits of mantissa without the leading 1
  XOR signs
  0 1010 000

## Slide 8: Multiplying floating point numbers
  sign exp fraction
  0 1001 010  1.01 x  5.000
  0 0111 110  1.11 x  * 1.75
  ----------------------- ------------ -----------
  0 1010 000  10.0011 x  8.75
  In this example, just to make a point, the fraction only has 3 binary digits so we can only record
  1.000 x as the answer which is 8.00 not 8.75

## Slide 9: Division in decimal and binary
5.25
4
20
------
1.0
.8
-------
.20
.20
--------
0
101.01
100
100
------
101
100
-------
100
100
--------
0

## Slide 10: Dividing floating point numbers
  sign exp fraction
  0 1001 0000  +4  1.0000 x
  0 1101 0101  +21  1.0101 x
  -------------------------------
  21/4 = 1.01010 x
  Convert from 2’s compliment to scientific notation
    - create mantissa by putting a 1 to the left of fraction
    - subtract bias (7) from the exponents
  Divide mantissas
  Subtract exponents
  Adjust exponent so mantissa starts 1.xxxx
  Add bias to exponent
  Fraction is the significant bits of mantissa without the leading 1
  XOR signs
  0 1010 000

## Slide 11: Dividing floating point numbers
  sign exp fraction
  0 1011 0101  1.0101 x  21.00
  0 1001 0000  1.00 x  4.00
  ----------------------- ------------ -----------
  0 1001 0101  1.0101 x  5.25
  In this example, just to make a point, the fraction only has 4 binary digits so we can record precisely
  1.0101 x as the answer which is 5.25

## Slide 12: Appendix A-1: Booth’s Algorithm
If we are going to multiply A*63
+63  0011 1111 which would require 6 shift/adds
Isn’t 63 = (64 – 1)?
So instead of A*63, we will do A*(64-1)
+64  0100 0000
So we do 1 add and 1 subtract (add 2’s compliment) instead of 6 adds.

## Slide 13: Appendix A-2: Booth’s Algorithm
+63  0011 1111 but isn’t 63 = (64 – 1)?
+7  0000 0111 but isn’t 7 = (8 – 1)?
63 – 7 = 0011 1111 – 000 0111 = 0011 1000 = 56
But isn’t 56 = (63 – 7) = (64 – 1) – (8 – 1) = 64 – 8?

## Slide 14: Appendix B: Multiply Overflow?
Suppose you multiplied 2 signed positive 8 bit numbers?
0001 0000 * 0001 0000 = 1 0000 0000 (overflow)
If both numbers have a bit on in the upper half, then there will be an overflow so there is no point in doing the multiplication. Therefore at least 1 number must have it’s upper half bits all set to 0.

## Slide 15: Appendix C: worst cast shift/adds
When multiplying 2-N bit positive numbers, at least 1 number must have it N/2 most significant bits = 0
What is the worst case of the number of shift/adds?
  N/2?
  Or less? (recall Booth’s algorithm can do N/2 consecutive 1’s with just 2 operations?
When multiplying 2-N bit positive numbers, at least 1 number must have it?
  The worst case is the lesser of straight multiplying vs. Booth’s